October 25, 2017 TMT Meeting

TMT Coordinated Chum Operation

1. EFFECTIVE NOVEMBER XX, AT 0600 HOURS, OPERATE THE

BONNEVILLE DAM TAILWATER IN THE FOLLOWING ORDER OF OPERATING

RANGES AS PROJECT OUTFLOW INCREASES.

2. DURING ALL HOURS, OPERATE PROJECT OUTFLOW TO PROVIDE A

TAILWATER ELEVATION IN THE RANGE OF 11.5-13.0 FEET.

3. THEN, IF NECESSARY TO INCREASE PROJECT OUTFLOW, THE

TAILWATER MAY BE OPERATED UP TO 16.5 FEET DURING NIGHTTIME

HOURS (1700-0600). CONCENTRATE HIGHEST ELEVATIONS AROUND

2400 HOURS.

5. THEN, IF NECESSARY TO INCREASE PROJECT OUTFLOW, THE

TAILWATER MAY BE OPERATED UP TO 18.5 FEET DURING NIGHTTIME

HOURS (1700-0600).

6. THEN, IF INCREASING RIVER FLOW PRECLUDES THE ABILITY TO

MANAGE TAILWATER WITHIN THE STEPS ABOVE, OPERATE TO PROVIDE

A TAILWATER IN THE RANGE OF 13.0-16.5 FEET DURING DAYTIME

HOURS (0600-1700) AND UP TO THE MAXIMUM WITHIN PROJECT

24-HOUR RAMP RATE LIMITS DURING NIGHTTIME HOURS (1700-0600).