OFFICIAL COORDINATION REQUEST

FOR

NON-ROUTINE OPERATIONS AND MAINTENANCE

Coordination Title: 12 IHR07 JCBS Outfall JSATS Hydrophone Installation

COORDINATION DATE -  06 July 2012

PROJECT- 	Ice Harbor Dam

RESPONSE DATE-  12 July 2012 FPOM Meeting

Description of the problem:

A tailrace tracking feasibility study is underway at Ice Harbor Dam under Contract# W912EF-08-D-0004, Task Order 0016. The purpose of this study is to determine the detection probability and 3D position precision and accuracy of fish carrying JSATS tags in the turbulent tailrace environment. The study will provide results that are spatially descriptive (both vertically and horizontally) of detection accuracy and precision within the tailrace regarding fish distribution and travel upon exiting turbine unit draft tubes, the JBS outfall, and the spillway.

The results of this study are applicable to tracking juvenile and adult salmonids and lamprey passage downstream, as well as adult salmonids and lamprey migration as they approach the dam and fishways. Perhaps the results relative to tracking adult salmonids and lamprey approaching the dam and facilities will provide insight for improvement of upstream migration and passage in the future.

For the purpose of covering the tailrace adequately and conducting the study as designed, hydrophones are to be installed at the terminus of the JBS outfall pipe in the tailrace at Ice Harbor Dam. Current project discharge creates an unsafe boating and equipment deployment conditions.

The results of this study are important for understanding fish migration behaviors at FCRPS dams. The timing of this operations modification request is largely due to an approximate two month delay in the kickoff of the study and the requirement of preliminary data collection to determine appropriate locations of hydrophones.

Type of outage required:

Shift spill to bays 6-10 (north spillway) for 6 hours (1000-1600). The desired date is 11 July 2012.

Impact on facility operation:

Currently Ice harbor Dam is under court-mandated summer spill operations. From June 21-July 13 required spill is 30%/30% (day/night) versus 45kcfs/Gas Cap (day/night). From July 13-August 31 required spill is 45kcfs/Gas cap (day/night). Shifting spill to the north spillway may impact TDG by shifting the full spill volume to the north side of the tailrace. It is not expected that adult attraction flows for the south fishway entrance will be affected; however, it is possible that the north fishway entrance will be difficult for adults to reach under increased spill.

Length of time for repairs:  N/A

Expected impacts on fish passage:

Daily average passage counts at the north and south fishways at Ice Harbor are detailed in tables below.  According to the adult counts between 6/26 and 7/05 the average number of adults passing via the north fishway is much fewer than those passing the south fishway. Of all adult fish passing during this time period approximately 2.5% of Chinook, 26.9% of steelhead, and 13.5% of sockeye passed via north fishway.

Diel adult passage counts do show the greatest portion of spring and summer Chinook, summer steelhead and sockeye are passing during the 1000-1600 window of the operations modification request. Snake River adult sockeye numbers have shown an increasing trend since 06/26.

Smolt passage at Lower Monumental Dam has shown a declining trend since 06/26 for CH0, CH1, and steelhead. On July 5th, 1037 CH0, 37 CH1, and 72 steelhead passed Lower Monumental and a total of 4 sockeye smolts since 6/26. These data are likely to reflect smolt passage at Ice Harbor as well.

If spill is shifted to the north spillway it is likely that tailrace egress conditions will deteriorate during the 6-hour request period. This may temporarily reflect poorly on smolt survival due to predation; however, with the fewer numbers of smolts passing Lower Monumental Dam any potential reduction in survival that may occur subsequent to a spill modification may be negligible.

Comments from agencies:

Final results:

Thank you,

Bradly A Trumbo

Fishery Biologist

Walla Walla District

509-527-7253

Table 1. North and south adult fishway counts at Ice Harbor Dam June 26-July 05 2012

| Ice Harbor South |
| --- |
| Date | All Chinook | Adult Chinook | Jack Chinook | All Steelhead | Clipped Steelhead | Unclipped Steelhead | All Coho | Adult Coho | Jack Coho | Sockeye | Chum | Pink |
| 6/26/2012 | 358 | 320 | 38 | 80 | 67 | 13 | 0 | 0 | 0 | 11 | 0 | 0 |
| 6/27/2012 | 353 | 329 | 24 | 38 | 31 | 7 | 0 | 0 | 0 | 5 | 0 | 0 |
| 6/28/2012 | 154 | 126 | 28 | 47 | 34 | 13 | 0 | 0 | 0 | 6 | 0 | 0 |
| 6/29/2012 | 241 | 218 | 23 | 30 | 28 | 2 | 0 | 0 | 0 | 8 | 0 | 0 |
| 6/30/2012 | 207 | 184 | 23 | 35 | 31 | 4 | 0 | 0 | 0 | 10 | 0 | 0 |
| 7/1/2012 | 149 | 133 | 16 | 42 | 37 | 5 | 0 | 0 | 0 | 8 | 0 | 0 |
| 7/2/2012 | 150 | 132 | 18 | 38 | 31 | 7 | 0 | 0 | 0 | 8 | 0 | 0 |
| 7/3/2012 | 202 | 180 | 22 | 39 | 25 | 14 | 0 | 0 | 0 | 11 | 0 | 0 |
| 7/4/2012 | 242 | 216 | 26 | 46 | 32 | 14 | 0 | 0 | 0 | 25 | 0 | 0 |
| 7/5/2012 | 210 | 184 | 26 | 139 | 92 | 47 | 0 | 0 | 0 | 25 | 0 | 0 |
| total | 2266 | 2022 | 244 | 534 | 408 | 126 | 0 | 0 | 0 | 117 | 0 | 0 |
| Average | 226.6 | 202.2 | 24.4 | 53.4 | 40.8 | 12.6 | 0 | 0 | 0 | 11.7 | 0 | 0 |
| Ice Harbor North |
| Date | All Chinook | Adult Chinook | Jack Chinook | All Steelhead | Clipped Steelhead | Unclipped Steelhead | All Coho | Adult Coho | Jack Coho | Sockeye | Chum | Pink |
| 6/26/2012 | 107 | 100 | 7 | 12 | 12 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 6/27/2012 | 204 | 192 | 12 | 29 | 23 | 6 | 0 | 0 | 0 | 1 | 0 | 0 |
| 6/28/2012 | 99 | 85 | 14 | 20 | 18 | 2 | 0 | 0 | 0 | 1 | 0 | 0 |
| 6/29/2012 | 101 | 88 | 13 | 17 | 11 | 6 | 0 | 0 | 0 | 1 | 0 | 0 |
| 6/30/2012 | 59 | 47 | 12 | 20 | 16 | 4 | 0 | 0 | 0 | 1 | 0 | 0 |
| 7/1/2012 | 39 | 32 | 7 | 11 | 7 | 4 | 0 | 0 | 0 | 0 | 0 | 0 |
| 7/2/2012 | 42 | 34 | 8 | 8 | 6 | 2 | 0 | 0 | 0 | 0 | 0 | 0 |
| 7/3/2012 | 89 | 66 | 23 | 33 | 25 | 8 | 0 | 0 | 0 | 5 | 0 | 0 |
| 7/4/2012 | 42 | 30 | 12 | 32 | 20 | 12 | 0 | 0 | 0 | 11 | 0 | 0 |
| 7/5/2012 | 14 | 13 | 1 | 15 | 11 | 4 | 0 | 0 | 0 | 0 | 0 | 0 |
| total | 796 | 687 | 109 | 197 | 149 | 48 | 0 | 0 | 0 | 20 | 0 | 0 |
| Average | 79.6 | 68.7 | 10.9 | 19.7 | 14.9 | 4.8 | 0 | 0 | 0 | 2 | 0 | 0 |

Table 2. Ice Harbor Dam average diel adult counts between aaproximately 04/01-08/31 (2005-2010)

|  | Spring Chinook | Summer Chinook | Summer Steelhead | Sockeye |
| --- | --- | --- | --- | --- |
| IHR N | 12.9 | 7.8 | 9.6 | 0.2 |
| IHR S | 47.6 | 3.6 | 23.2 | 0.04 |

Table 3. Lower Monumental smolt passage data June 26-July 05, 2012

| Date | CH0 | CH1 | STH | SOCK |
| --- | --- | --- | --- | --- |
| 06/26/12 | 12670 | 338 | 319 | 1 |
| 06/27/12 | 13264 | 149 | 529 | 0 |
| 06/28/12 | 16014 | 307 | 399 | 0 |
| 06/29/12 | 7415 | 5866 | 0 | 0 |
| 06/30/12 | 5676 | 789 | 153 | 0 |
| 07/01/12 | 4864 | 16 | 157 | 0 |
| 07/02/12 | 5982 | 159 | 2 | 0 |
| 07/03/12 | 5078 | 181 | 315 | 2 |
| 07/04/12 | 3265 | 150 | 147 | 1 |
| 07/05/12 | 1037 | 37 | 72 | 0 |