OFFICIAL COORDINATION REQUEST

FOR

NON-ROUTINE OPERATIONS AND MAINTENANCE

COORDINATION TITLE – 12LMN05 SMCAP prefilter

COORDINATION DATE- 	4/25/12

PROJECT- 	Lower Monumental Dam

RESPONSE DATE-  May FPOM

Description of the problem:	  At the time the FPP and Appendix A was drafted; the small cap project for the lube oil prefilters was not funded.  The project is fully funded and scheduled.  The funding has to be used up by the end of the fiscal year.  All the units work has been scheduled in conjunction with other outages.  However;  main unit 3 will need a separate day long outage to execute the work.

Type of outage required:  Main unit 3 on June 11, 2012

Impact on facility operation:  LoMo will have to deviate from unit priority (para 4.1).  Unit 3 is the second in line and with the amount of water in June,  Unit 3 will be in service.

Length of time for repairs:  1 day

Expected impacts on fish passage:  Adult spring chinook migration peaks at Lower Monumental Dam as early as 4/20 and as late as 5/27 (FPP Table LMN-4, page LNM-5).  The proposed work is scheduled after this period and before the historic peak dates for the adult summer chinook migration.  Summer chinook runs peak as early as 6/14 and as late as 7/12. Expected flows will allow units 1 and 2 to operate thus keeping attraction of adult fish strongly to the north fishway entrances.  We have chosen the date based upon adult return dates and availability of manpower to do the work.  This work will be done outside the barrel of the unit thus replacing a potential source point for oil introduction into the river with a no risk location.

Comments from agencies

Final results:

Thank you,