# FPP Change Request Form

Change Request Number: 14BON001 Table BON-16 inclusion of mid range

Date Submitted:  6 March 2013

Project: BON

Requester Name, Agency: FPOM BON Ops Task Group

Location of Change: BON 5.2 and 5.3, Table BON-16 (re-numbering will occur as needed)

Proposed Change:

5.2. November 1 through March 31.  All turbine units will operate within 1% of best efficiency as a soft constraint.

5.3. April 1 through October 31.  All turbine units will operate within the 1% range as a hard constraint at various head ranges as shown in Table BON-15 and Table BON-16, except as define in 5.3.1.

5.3.1 April 10 through August 31.  Operate in the following priority order to pass increasing flow:

- Spill at the FOP limit.  (see Appendix E)

- Operate PH2 at the mid-range, as defined in Table BON-16;

- Operate PH1 at the upper end of 1%;

- Operate PH1 up to Best Operating Point (BOP);

- From April 10 through June 20.  As flows increase the adult/juvenile spring Chinook trigger (adult counts exceed juvenile collection counts for two consecutive days) will be implemented in one of the following ways, as directed by Project Fisheries:

A.  If the adult triggers are met (adult counts exceed juvenile collection counts for two consecutive days) the additional flow will be put through PH2 units.  PH2 will be operated up to the upper 1%, with unit generation increasing in the following order: 18, 17, 16, 15, 14, 13, 12, 11

B.  If the adult trigger is not met (adult counts are less than juvenile collection counts for two consecutive days) the additional flow will be put through the spillway.

Table BON-16.  Bonneville Dam Powerhouse Two Turbine Units 11-18 (with and without STSs) Output (MW) and Discharge (cfs) at the Upper and Lower Limits of the 1% of Peak Efficiency Operating Range.

| Head (feet) | Powerhouse Two (units 11-18) |
| --- | --- |
|  | With STS | Without STS |
|  | Lower 1% Limit | Mid Range 13K – 15K | Upper 1% Limit | Lower 1% Limit | Mid Range | Upper 1% Limit |
|  | (MW) | (cfs) | (MW) | (MW) | (MW) | (cfs) | (MW) | (cfs) | (MW) | (cfs) | (MW) | (cfs) |
| 35 | 27.6 | 11,259 | 31.9 | 36.8 | 44.3 | 18,068 | 28.2 | 11,444 | 36.7 | 14,861 | 45.1 | 18,277 |
| 36 | 28.5 | 11,271 | 32.9 | 37.9 | 45.8 | 18,097 | 29.2 | 11,455 | 37.9 | 14,881 | 46.6 | 18,306 |
| 37 | 29.4 | 11,279 | 33.9 | 39.1 | 47.3 | 18,121 | 30.1 | 11,464 | 39.1 | 14,898 | 48.1 | 18,331 |
| 38 | 30.3 | 11,284 | 34.9 | 40.3 | 48.8 | 18,139 | 31.0 | 11,470 | 40.4 | 14,910 | 49.7 | 18,350 |
| 39 | 31.3 | 11,287 | 36.0 | 41.6 | 50.3 | 18,153 | 32.0 | 11,473 | 41.6 | 14,919 | 51.2 | 18,364 |
| 40 | 32.2 | 11,288 | 37.1 | 42.8 | 51.8 | 18,162 | 32.9 | 11,474 | 42.8 | 14,924 | 52.7 | 18,374 |
| 41 | 33.0 | 11,259 | 38.1 | 44.0 | 53.3 | 18,197 | 33.7 | 11,445 | 44.0 | 14,927 | 54.3 | 18,409 |
| 42 | 33.8 | 11,230 | 39.1 | 45.2 | 54.9 | 18,228 | 34.6 | 11,415 | 45.2 | 14,928 | 55.8 | 18,441 |
| 43 | 34.6 | 11,201 | 40.2 | 46.3 | 56.4 | 18,255 | 35.4 | 11,386 | 46.4 | 14,927 | 57.4 | 18,468 |
| 44 | 35.4 | 11,172 | 41.2 | 47.5 | 57.9 | 18,278 | 36.2 | 11,357 | 47.6 | 14,925 | 58.9 | 18,493 |
| 45 | 36.2 | 11,144 | 42.2 | 48.7 | 59.4 | 18,299 | 37.0 | 11,328 | 48.8 | 14,921 | 60.5 | 18,514 |
| 46 | 37.0 | 11,139 | 43.2 | 49.8 | 61.0 | 18,366 | 37.9 | 11,324 | 50.0 | 14,953 | 62.1 | 18,581 |
| 47 | 37.8 | 11,135 | 44.2 | 51.0 | 61.9 | 18,200 | 38.7 | 11,319 | 50.9 | 14,867 | 63.0 | 18,415 |
| 48 | 38.7 | 11,129 | 45.2 | 52.1 | 62.7 | 18,040 | 39.6 | 11,314 | 51.7 | 14,785 | 63.8 | 18,255 |
| 49 | 39.5 | 11,124 | 46.2 | 53.3 | 63.5 | 17,887 | 40.4 | 11,308 | 52.6 | 14,705 | 64.7 | 18,101 |
| 50 | 40.3 | 11,118 | 47.2 | 54.4 | 67.5 | 18,598 | 41.3 | 11,303 | 55.0 | 15,060 | 68.7 | 18,817 |
| 51 | 41.3 | 11,154 | 48.1 | 55.5 | 69.8 | 18,850 | 42.2 | 11,339 | 56.7 | 15,206 | 71.1 | 19,072 |
| 52 | 42.3 | 11,187 | 49.1 | 56.7 | 72.1 | 19,091 | 43.2 | 11,373 | 58.3 | 15,345 | 73.4 | 19,316 |
| 53 | 43.2 | 11,219 | 50.1 | 57.8 | 74.5 | 19,323 | 44.2 | 11,405 | 60.0 | 15,478 | 75.8 | 19,551 |
| 54 | 44.2 | 11,249 | 51.0 | 58.8 | 76.5 | 19,536 | 45.2 | 11,436 | 60.9 | 15,434 | 76.5 | 19,431 |
| 55 | 45.2 | 11,278 | 52.1 | 60.1 | 76.5 | 19,115 | 46.2 | 11,466 | 61.4 | 15,221 | 76.5 | 18,975 |
| 56 | 46.4 | 11,343 | 53.2 | 61.3 | 76.5 | 18,718 | 47.4 | 11,531 | 62.0 | 15,056 | 76.5 | 18,581 |
| 57 | 47.6 | 11,404 | 54.2 | 62.6 | 76.5 | 18,336 | 48.6 | 11,593 | 62.6 | 14,898 | 76.5 | 18,202 |
| 58 | 48.8 | 11,461 | 55.4 | 63.9 | 76.5 | 17,967 | 49.9 | 11,652 | 63.2 | 14,744 | 76.5 | 17,836 |
| 59 | 50.0 | 11,515 | 56.5 | 65.1 | 76.5 | 17,611 | 51.1 | 11,707 | 63.8 | 14,595 | 76.5 | 17,483 |
| 60 | 51.2 | 11,567 | 57.6 | 66.4 | 76.5 | 17,267 | 52.3 | 11,760 | 64.4 | 14,451 | 76.5 | 17,142 |
| 61 | 51.8 | 11,532 | 58.5 | 67.5 | 76.5 | 16,978 | 53.0 | 11,724 | 64.8 | 14,291 | 76.5 | 16,857 |
| 62 | 52.5 | 11,498 | 59.5 | 68.6 | 76.5 | 16,699 | 53.7 | 11,690 | 65.1 | 14,136 | 76.5 | 16,582 |
| 63 | 53.1 | 11,466 | 60.4 | 69.7 | 76.5 | 16,428 | 54.3 | 11,657 | 65.4 | 13,986 | 76.5 | 16,315 |
| 64 | 53.7 | 11,434 | 61.3 | 70.7 | 76.5 | 16,166 | 55.0 | 11,625 | 65.8 | 13,841 | 76.5 | 16,056 |
| 65 | 54.4 | 11,405 | 62.3 | 71.8 | 76.5 | 15,912 | 55.6 | 11,595 | 66.1 | 13,701 | 76.5 | 15,806 |
| 66 | 55.4 | 11,448 | 63.2 | 72.9 | 76.5 | 15,671 | 56.7 | 11,639 | 66.6 | 13,605 | 76.5 | 15,570 |
| 67 | 56.5 | 11,490 | 64.2 | 74.0 | 76.5 | 15,437 | 57.8 | 11,682 | 67.2 | 13,512 | 76.5 | 15,341 |
| 68 | 57.5 | 11,532 | 65.1 | 75.1 | 76.5 | 15,210 | 58.9 | 11,724 | 67.7 | 13,422 | 76.5 | 15,119 |
| 69 | 58.6 | 11,571 | 66.1 | 76.3 | 76.5 | 14,990 | 59.9 | 11,764 | 68.2 | 13,334 | 76.5 | 14,903 |
| 70 | 59.6 | 11,610 | 67.0 | 77.3 | 76.5 | 14,775 | 61.0 | 11,803 | 68.8 | 13,248 | 76.5 | 14,693 |

*  Table based on data provided by HDC, January 2001 (Table BON-16 revised 2006).

Justification for Change:

FPOM requested the mid-range columns be added since PH2 may be limited to the mid-range operation.

Comments from others (Date – Name – Comments):

Record of Final Action (Date – Action):