COORDINATION TITLE: 13 MCN 02 McNary FGE study

COORDINATION DATE-14 February 2013

PROJECT- McNary

Description of the problem:

A fish guidance efficiency (FGE) and fish condition study relative to partially raised operating gate (PROG) and stored operating gate (SOG) position will occur at McNary Dam during the 2013 fish passage season. The study will occur over a period of approximately two weeks during April-May, and again in June-July. Prior to the fish passage season, hydroacoustic transducers will be installed behind the trashracks and on the ESBS brackets in the A, B, and C intakes in turbine units 6, 7, 12, and 13 (assuming units 4 and 11 will be OOS for rewind).

Intake gate positions will be alternated among two turbine pairs for all three intakes of each turbine during the study. One unit of each pair will have all gates in the SOG position while the other unit will have all gates in the PROG position. Gate positions will need to be switched once during the April-May period, and again during the June-July period. Currently unit 6 intake gates are lowered at the beginning of each month to address an oil leak in the turbine hub. This will be considered in the study design to reduce the number of times the intake gates need to be moved. Turbine units will be operated at peak efficiency or upper 1% and may need to be changed to the appropriate operation at times.

No fish condition evaluation component will be implemented during this study.

Type of outage required:

The use of turbines 6 and 7 may cause unit priority to deviate from that stated in the FPP and should be coordinated through FPOM. It is expected that the install of hydroacoustic transducers behind the trashrack will require approximately 7 days and occur between 11 February and 4 March, 2013. Divers will not be behind the trashrack at any time.

Turbine units may need to be operated at a specific load within the 1% operating range at times depending upon the day and treatment. This will need to be coordinated through the project, as well as FPOM.

Requiring head gates to be lowered during fish passage season for the study will deviate from the FPP August 1-December 15 time period for gates being lowered. The study design will also consider leaving the intake gates in the last treatment position of the spring period and beginning the summer period with this configuration.

Impact on facility operation:

The installation of hydroacoustic transducers and changing of turbine operations will require operational support from the project. Outages during install of hydroacoustic transducers will be required. Turbines will be operated within the 1% range, but will require operating adjustments. Movement of head gate position will require project personnel and potentially unit outages.

Length of time for repairs:  N/A

Expected impacts on fish passage:

Installing gear will occur prior to fish passage season, and removal will occur at the end of the season and should not affect fish passage. Changing of turbine operations within the 1% range should not affect fish passage.

Changes in head gate configuration and potential outages required to make the changes may temporarily reduce FGE in the affected units. Leaving head gates in the SOG position in two units between spring and summer studies for a period of approximately 5 weeks between 12 May and 15 June will reduce FGE and may affect smolt survival. Estimates of the potential impact to migrating yearling Chinook and steelhead smolts have been generated for Snake River and Mid and Upper Columbia River yearling Chinook and steelhead (See attached figures and tables).

Comments from agencies

.

Final results

Affects of leaving head gates in the SOG position in two units between 12 May and 15 June, 2013.

Lowered head gates in two units at McNary Dam for a 5 week period between spring and summer FGE samples may reduce FGE and increase mortality associated with turbine passed fish. To approximate the proportion of migrating smolts that may be affected by leaving head gates down in two units for 5 weeks, estimates of the total number of Snake River and mid and upper Columbia River yearling Chinook salmon, juvenile steelhead and sockeye salmon arriving at McNary Dam were averaged among 2010, 2011, and 2012. These estimates were reported in the NOAA Fisheries Northwest Fisheries Science Center 2010, 2011, and 2012 memorandums (Table 1). The average numbers of smolts arriving at McNary were then applied to a simple equation that accounted for spill passage proportion, bypass and turbine survival estimates (2006-2009 data used for McNary COP), estimated proportion of the run that will pass during the 5 week period of interest, estimated turbine passage proportion, and an assumed 3% reduction in FGE for two turbine units (Swan and Norman 1987).

Table 1 Combined (wild and hatchery) number of smolts estimated arriving at McNary Dam in 2010, 2011, and 2012 (NOAA 2010, 2011, 2012). CH1=yearling Chinook, STH=steelhead smolts, SOC=sockeye smolts, Snake=Snake River, Col=Mid and Upper Columbia stocks combined.

|  | CH1 Snake | CH1 Col | STH Snake | STH Col | SOC* |
| --- | --- | --- | --- | --- | --- |
| 2010 | 2,121,507 | 5,635,156 | 859,774 | 1,274,247 | 401,215 |
| 2011 | 2,337,725 | 5,160,066, | 1,298,936 | 1,378,891 | 426,726 |
| 2012 | 2,269,194 | 5,781,775 | 1,064,901 | 1,571,481 | 391,162 |
| Mean | 2,242,809 | 5,708,466 | 1,074,537 | 1,408,206 | 406,368 |

*Because of extreme year-to-year variability, the count used at McNary Dam for sockeye in 2010 was based on the average of the counts at the dam from 1988 to 2009; 2011 was based on the average of the counts at the dam from 1988 to 2010; 2012 was based on the average of the counts at the dam from 1990 to 2011 (NOAA 2010, 2011, 2012).

Yearling Chinook

Assumptions:

- ~2,242,809 Snake River yearling Chinook and ~5,708,466 Mid and Upper Columbia River yearling Chinook will arrive at McNary Dam

- ~48% of the run will arrive during the 5 week period with head gates in the SOG position (Figures 1-3)

- Spill passage efficiency will be ~65% leaving 35% of the run exposed to the powerhouse and ~13% pass turbines (2006-2009 data used for McNary COP)

- FGE reduction ~3% (Swan and Norman 1987)

~87% turbine survival and ~100% bypass survival

Equation 1:	(5708466*0.43*(0.7*0.13)*(2/14)*0.03*(0.98-0.87))

Equation 1 was used to provide the following estimates of increased mortality for yearling Chinook salmon using the mean smolt numbers from Table 1. Given the assumptions for yearling Chinook are correct and an approximate 3% reduction in FGE occurs because the head gates are left in the SOG position for 5 weeks in two turbine units these estimates are realistic.

Table 2: Estimated increased percentage of the yearling Chinook run that may experience mortality with an FGE reduction of 3% in two turbine units. FGE reduction is caused by having head gates in the SOG position for 5 weeks between 12 May and 15 June, 2013. Estimates were generated for various spill passage proportions to encompass the mean 65% from 2006-2009 McNary data.

| Snake and Columbia River Yearling Chinook Potential Increased Mortality |
| --- |
|  |  | Proportion Spill Passage |  |
|  |  | 30 | 40 | 50 | 60 | 70 |  |
|  | Percentage of Run | 0.0024% | 0.0021% | 0.0017% | 0.0014% | 0.0010% |  |

Juvenile Steelhead

Assumptions:

- ~1,074,537 Snake River juvenile steelhead and ~1,408,206 Mid and Upper Columbia River juvenile steelhead will arrive at McNary Dam

- ~31% of the run will arrive during the 5 week period with head gates in the SOG position (Figures 4-6)

- Spill passage efficiency will be ~49% leaving 51% of the run exposed to the powerhouse (2006-2009 data used for McNary COP)

- Turbine passage proportion ~13% (2006-2009 data used for McNary COP)

- FGE reduction ~3% (Swan and Norman 1987)

- ~77% turbine survival; ~100% bypass survival

Equation 1 was used to provide the following estimates of increased mortality for juvenile steelhead using the mean smolt numbers from Table 1. Given the assumptions for steelhead are correct and an approximate 3% reduction in FGE occurs because the head gates are left in the SOG position for 5 weeks in two turbine units these estimates are realistic.

Table 3 Estimated increased percentage of the juvenile steelhead run that may experience mortality with an FGE reduction of 3% in two turbine units. FGE reduction is caused by having head gates in the SOG position for 5 weeks between 12 May and 15 June, 2013. Estimates were generated for various spill passage proportions to encompass the mean 49% from 2006-2009 McNary data.

| Columbia and Snake River Steelhead Potential Increased Mortality |
| --- |
|  | Proportion Spill Passage |
|  | 30 | 40 | 50 | 60 | 70 |
| Percentage of Run | 0.0019% | 0.0017% | 0.0014% | 0.0011% | 0.0008% |

Juvenile Sockeye

Assumptions:

- ~406,368 Columbia and Snake River juvenile Sockeye will arrive at McNary Dam (NOAA 2010, 2011, 2012)

- ~62% of the run will arrive during the 5 week period with head gates in the SOG position (Figures 7-9)

- Spill passage efficiency will be ~68% leaving 32% of the run exposed to the powerhouse (Adams et al. 2011; Table 4)

- FGE reduction ~3% (Swan and Norman 1987)

- ~93% powerhouse survival and ~94% spillway survival (Adams et al. 2011; Table 4)

Table 4 Passage and survival probabilities for sockeye smolts at McNary Dam (Adams et al. 2011)

| McNary 2006-2009 Sockeye Survival Probabilities |
| --- |
|  |  | PH | Spillway | Spill Prop |  |
|  | 2006 | 92.6% | 83.6% | 67% |  |
|  | 2007 | 98.6% | 104.3% | 61% |  |
|  | 2008 | 85.8% | 92.5% | 80% |  |
|  | 2009 | 93.0% | 95.9% | 63% |  |
|  | Mean | 92.50% | 94.08% | 68% |  |

Equation 2:	(406368*0.62*(0.7*0.32)*(2/14)*0.03*(0.94-0.925))

Equation 2 was used to provide the following estimates of increased mortality for juvenile steelhead using the mean smolt numbers from Table 1. Given the assumptions for steelhead are correct and an approximate 3% reduction in FGE occurs because the head gates are left in the SOG position for 5 weeks in two turbine units these estimates are realistic. Bypass and turbine survival estimates were not available for sockeye; hence, powerhouse and spillway survival estimates were used as surrogates for these parameters and may not be completely representative of survival through the turbines or bypass system.

Table 5 Estimated increased percentage of the juvenile steelhead run that may experience mortality with an FGE reduction of 3% in two turbine units. FGE reduction is caused by having head gates in the SOG position for 5 weeks between 12 May and 15 June, 2013. Estimates were generated for various spill passage proportions to encompass the mean 68% (Adams et al. 2011).

| Columbia and Snake River Sockeye Potential Increased Mortality |
| --- |
|  | Proportion Spill Passage |
|  | 30 | 40 | 50 | 60 | 70 |
| Percentage of Run | 0.0009% | 0.0008% | 0.0006% | 0.0005% | 0.0004% |

Figure 1 Yearling Chinook salmon 2010 smolt passage index used to estimate proportion of the run passing McNary during the 5 week period of 12 May through 15 June requested to leave head gates in the SOG position in two turbine units for the FGE study.

Figure 2 Yearling Chinook salmon 2011 smolt passage index used to estimate proportion of the run passing McNary during the 5 week period of 12 May through 15 June requested to leave head gates in the SOG position in two turbine units for the FGE study.

Figure 3 Yearling Chinook salmon 2012 smolt passage index used to estimate proportion of the run passing McNary during the 5 week period of 12 May through 15 June requested to leave head gates in the SOG position in two turbine units for the FGE study.

Figure 4 Juvenile steelhead 2010 smolt passage index used to estimate proportion of the run passing McNary during the 5 week period of 12 May through 15 June requested to leave head gates in the SOG position in two turbine units for the FGE study.

Figure 5 Juvenile steelhead 2011 smolt passage index used to estimate proportion of the run passing McNary during the 5 week period of 12 May through 15 June requested to leave head gates in the SOG position in two turbine units for the FGE study.

Figure 6 Juvenile steelhead 2012 smolt passage index used to estimate proportion of the run passing McNary during the 5 week period of 12 May through 15 June requested to leave head gates in the SOG position in two turbine units for the FGE study.

Figure 7 Juvenile wild Sockeye 2010 smolt passage index used to estimate proportion of the run passing McNary during the 5 week period of 12 May through 15 June requested to leave head gates in the SOG position in two turbine units for the FGE study.

Figure 8 Juvenile wild Sockeye 2011 smolt passage index used to estimate proportion of the run passing McNary during the 5 week period of 12 May through 15 June requested to leave head gates in the SOG position in two turbine units for the FGE study.

Figure 9 Juvenile wild Sockeye 2012 smolt passage index used to estimate proportion of the run passing McNary during the 5 week period of 12 May through 15 June requested to leave head gates in the SOG position in two turbine units for the FGE study.

References

Adams, N.S., and Evans, S.D., eds., 2011, Summary of juvenile salmonid passage and survival at McNary Dam—Acoustic survival studies, 2006–09: U.S. Geological Survey Open-File Report 2011-1179.

(NOAA) National Oceanic and Atmospheric Administration. 2010. Memorandum: Estimation of Percentages for Listed Pacific Salmon and Steelhead Smolts Arriving at Various Locations in the Columbia River Basin in 2010. Northwest Fisheries Science Center, Seattle, Washington.

(NOAA) National Oceanic and Atmospheric Administration. 2011. Memorandum: Estimation of Percentages for Listed Pacific Salmon and Steelhead Smolts Arriving at Various Locations in the Columbia River Basin in 2011. Northwest Fisheries Science Center, Seattle, Washington.

(NOAA) National Oceanic and Atmospheric Administration. 2012. Memorandum: Estimation of Percentages for Listed Pacific Salmon and Steelhead Smolts Arriving at Various Locations in the Columbia River Basin in 2012. Northwest Fisheries Science Center, Seattle, Washington.

Swan, G. A., and W. T. Norman. 1987. Research to improve subyearling Chinook salmon fish guiding efficiency at  McNary Dam, 1986. Report of the National Oceanic and Atmospheric Administration to the US Army Corps of Engineers, Walla Walla, Washington, under Contract DACW68-84-H-0034.

# Text boxes

Mean # of stocks arriving at McNary Dam from Table 1

Run Proportion passing 12 May- 15 June

FGE differential

Bypass-turbine survival differential

Powerhouse*turbine proportions

2 of 14 turbines affected by reduced FGE

Mean # of stocks arriving at McNary Dam from Table 1

Run Proportion passing 12 May- 15 June

FGE differential

Spillway-Powerhouse survival differential

Powerhouse*turbine proportion

2 of 14 turbines affected by reduced FGE