OFFICIAL COORDINATION REQUEST

FOR

NON-ROUTINE OPERATIONS AND MAINTENANCE

COORDINATION TITLE:  13 MCN 01 Adult Steelhead Direct Injury and Survival through the TSW and Turbines.

COORDINATION DATE- 	7 January 2013

PROJECT- 	McNary

RESPONSE DATE-  FPOM meeting  Jan. 10, 2013

Description of the problem:

Direct injury and survival estimation of adult steelhead passing turbines and temporary spillway weirs (TSW) will occur at McNary during March, 2013. It is expected that TSW’s will need to be installed in spill bays 19 and 20 beginning by 18 February, 2013. The FPP does not specify an installation date for the TSW’s but simply states that the TSW’s must be available for the start of the fish passage season. The TSW’s will operate up to 10kcfs in bay 20.  It is expected that the study will begin by 11 March, 2013 and will require approximately three weeks for completion. Upon the completion of the study it is expected that the TSW’s will remain in place for the fish passage season beginning in early April. Turbine unit 12A will be used for the study and turbine operations have been identified as peak efficiency and best geometry (approximately 14kcfs). Turbines operate under the 1% soft constraint between November 1 and March 31; however, operation at the best geometry point (~14kcfs) will be coordinated through FPOM. Equipment removal will occur prior to the beginning of the fish passage season and is expected during the last week of March and first week of April.

Type of outage required:

Turbine unit 12 outage may be required to install the direct release pipe structure in the head gate slot of intake A. Operation at ~14kcfs will need approval through FPOM and BPA. Spill requirements for the TSW in bay 20 will need approval through FPOM and BPA.

Impact on facility operation:

The study will potentially require the flat bed truck to move the fish release apparatus from the bone yard to the powerhouse deck. Project personnel and the use of the gantry crane will be required for install and removal of the fish release structure as well. Operations assistance for changing turbine operations will be required. These requirements may be difficult for the project to support and is currently being coordinated through McNary personnel.

Length of time for repairs:  N/A

Expected impacts on fish passage:

The study is expected to be completed with equipment removed prior to the beginning of fish passage season with no expected impact on fish passage.

Comments from agencies

Final results:

Thank you,