## Slide 1: Adult Spring Chinook Salmon Passage and Migration Behavior through the Lower Snake River (gas cap spill evaluation)
Daniel Deng, Jayson Martinez, Tao Fu, Robert Mueller, Brett Pflugrath, Christopher Grant, Ryan Harnish, Xinya Li, Scott Titzler, Kenneth Ham, Xinming Lin, Huidong Li

## Slide 2: Outline
Study Objectives
Fish Collection and Tagging
Detection Arrays
Controlled Testing
Preliminary Results
Conclusions

## Slide 3: Study Objectives
Evaluate tailrace movements, passage, and fallback of adult Chinook salmon at Little Goose Dam (LGS) in relation to increased spill levels
  Metrics for the consequence of spill include:
    Tailrace behavior and movement
    Behavior in relation to operations and hydraulic conditions
    Delay/holding tailrace locations
    Preferred entrances into the adult fish ladder
  Calculate relevant adult passage metrics to compare against the previous radio telemetry results by Clabough et al. (2014) and Jepson et al. (2009).
A component of this study included using the data collected to conduct a post-construction evaluation of a new adult ladder passage temperature reduction system.

## Slide 4: Fish Collection and Tagging
Fish Collection and Tagging

## Slide 5: Fish Trap
Modified from USACE Walla Walla District

## Slide 6: Fish Tagging Summary
400 Fish tagged
  Both AT and PIT
April 26th – June 6th
1.3% of the run
Released same day as tagging
Chart: Number of fish tagged
| 43208 | 43209 | 43210 | 43211 | 43212 | 43213 | 43214 | 43215 | 43216 | 43217 | 43218 | 43219 | 43220 | 43221 | 43222 | 43223 | 43224 | 43225 | 43226 | 43227 | 43228 | 43229 | 43230 | 43231 | 43232 | 43233 | 43234 | 43235 | 43236 | 43237 | 43238 | 43239 | 43240 | 43241 | 43242 | 43243 | 43244 | 43245 | 43246 | 43247 | 43248 | 43249 | 43250 | 43251 | 43252 | 43253 | 43254 | 43255 | 43256 | 43257 | 43258
# tagged | 1 | 2 | 4 | 3 | 7 | 3 | 9 | 9 | 6 | 15 | 24 | 37 | 37 | 40 | 39 | 15 | 22 | 20 | 20 | 19 | 20 | 14 | 15 | 10 | 9
Fish Passed | 5 | 4 | 5 | 2 | 2 | 4 | 3 | 1 | 8 | 5 | 8 | 8 | 18 | 19 | 19 | 38 | 42 | 112 | 250 | 297 | 148 | 274 | 619 | 635 | 1118 | 1503 | 1634 | 1603 | 873 | 837 | 482 | 809 | 1666 | 1039 | 976 | 1143 | 725 | 891 | 594 | 1696 | 1278 | 1631 | 1099 | 467 | 320 | 1272 | 1047 | 871 | 740 | 700 | 624 | 350 | 673 | 817 | 586 | 406 | 249 | 239
Chart: Length grouping (mm)
| 600-650 | 650-700 | 700-750 | 750-800 | 800-850 | 850-900 | 900-950 | 950-1000 | 1000+
Clipped | 7 | 61 | 123 | 87 | 14 | 1 | 1 | 0 | 0
Unclipped | 11 | 26 | 34 | 25 | 6 | 2 | 1 | 0 | 1
~25% unclipped fish

## Slide 7: “Sturgeon” Tag (Small long-life acoustic transmitter)
Dimension: 24.2 mm x 5.0 mm
Dry Weight: 0.7 g
Wet Weight: 0.2 g
Volume: 429 mm3
Source Level: 161 or 163 dB at zero degrees
Configurable source level, pulse rate interval, & tag code.
Tag Life:
  30 days at 163 dB and 2-s pulse rate interval
  365 days at 161 dB and 15-s pulse rate interval.

## Slide 8: Detection Arrays
Detection Arrays

## Slide 9: LGS Deployment

## Slide 10: Autonode and PIT Arrays

## Slide 11: Controlled Testing
Controlled Testing

## Slide 12: Error Analysis - 32 Test Locations
River Flow

## Slide 13: New 2D/3D Hybrid Solver
3D: Requires decodes from at least 4 hydrophones, produces X,Y,Z
2D: Requires decodes from at least 3 hydrophones, produces X,Y
Current solver, 3D only
New Solver, 2D and 3D hybrid tracks
  More Tracks
  Similar Accuracy along X and Y

## Slide 14: Improvement: New 2D/3D Hybrid Solver
LGS18_Block02-04_Adult_Fish | 3D | 2D/3D Hybrid | Diff
# Tag has Track | 140 | 212 | 72 (51%)
total # of Track | 3206 | 14578 | 11372 (355%)
3D Solver
2D/3D Hybrid Solver

## Slide 15: Preliminary Results
Preliminary Results

## Slide 16: Detection and Tracking Summary in Different Regions
 | Number of Detected Fish | Median Number of Detections | Number of Tracked Fish | Median of Tracked Locations
LGS Tailrace Cabled /LGS Tailrace Auto | 369 | 7325 | 345 | 128
LGS Tailrace Cabled | 311 | 162 | 228 | 13
LGS Tailrace Cabled - Outfall | 147 | 36 | - | -
LGS Tailrace Cabled - South Wall | 300 | 141 | - | -
LGS Tailrace Cabled - Powerhouse | 167 | 18 | - | -
LGS Tailrace Auto | 331 | 8397 | 316 | 123
LGS Tailrace Auto - North Shore | 330 | 8387 | 316 | 123
LGS Tailrace Auto - Downstream Outfall | 59 | 18 | - | -
LGS Tailrace Auto - Upstream Outfall* | - | - | - | -
LGS Forebay Cabled | 342 | 166 | 282 | 18
LGR Forebay Cabled | 340 | 910 | 325 | 59
* No valid data was collected |  |  |  | 

## Slide 17: First LGS Tailrace Detections and Fish Ladder Entrance
Outfall | South Wall | Powerhouse Tailrace | North Shore Tailrace | Total
40 | 90 | 10 | 229 | 369
11% | 24% | 3% | 62% | 
Entry Location** | 2008 | 2013 | 2018
South Powerhouse | 138 (48%) | 170 (64%) | 163 (47%)
North Powerhouse | 25 (9%) | 44 (16%) | 3 (1%)
North Shore | 123 (43%) | 53 (20%)* | 182 (52%)
Unknown |  |  | 1 (0.25%)
Total | 286 | 267 | 349
* Reported as unknown because the north shore was unmonitored during study. |  |  | 
** The first fish ladder entry detection location for each fish: based on the detection of the receivers at each entrance inside the fish ladder. |  |  | 
First LGS Tailrace Detections
First LGS Fish Ladder Entrance
27.5%
11.5%
12%
50%
Staying near Northshore before entering fish ladder
Staying near Southshore before entering fish ladder
Swim between regions before entering fish ladder

## Slide 18: Fish Track and Time Lapse Video

## Slide 19: North Shore Fish Tracks

## Slide 20: Fish Passage Detections at Each Dam
Location | 2008 | 2013(1) | 2018 | 2018 (PIT)
Release | 360 | 300 | 400 | 400
Passed Lower Monumental |  | 264 (88.0%) | 387 (96.8%)(2) | 360 (90.0%)
At Little Goose | 290 (80.6%) | 261 (87.0%) | 369 (92.3%) (3) | 
Passed Little Goose | 287 (79.7%) | 256 (85.3%) | 367 (91.8%) (4) | 353 (88.3%)
Passed Lower Granite |  | 252 (84.0%) | 364 (91.0%) (5) | 354 (88.5%)
(1) Includes both RT and PIT |  |  |  | 
(2) Detected by LMN PIT or any LMN upstream PIT/Auto/Cabled arrays |  |  |  | 
(3) Detected by either LGS tailrace cabled array or LGS near dam auto nodes |  |  |  | 
(4) Detected by any LGS upstream arrays (LGS PIT, LGS FL exit, LGS forebay cabled, LGR PIT, or LGR forebay cabled array) |  |  |  | 
(5) Detected by either LGR forebay cabled array or LGR PIT detectors |  |  |  | 

## Slide 21: Median Fish Passage Times
From first tailrace detection to… | 2008* | 2013 | 2018
First fishway entry detection (hrs) | 7.3/11.8/5.5 | 7.4 | 13
Exit to LGS forebay (hrs) | 14.5/21.6/11.5 | 19.7 | 25.0**
First fishway entry to ladder top (hrs) | 3.5/2.9/3.1 |  | 3.2
* Separated by 3 different spill patterns (Alternate, Bulk, Uniform) |  |  | 
** From first tailrace detection time to the first fish ladder exit detection time |  |  | 

## Slide 22: Fallback at LGS
 | 2008 | 2013 | 2018
Fallback percent* | 3.9% | 7.5% | 9.8%
Fallback rate** | 5.3% | 7.9% | 12.0%
*unique fish that fell back/unique fish passed dam |  |  | 
**fallback events/unique fish passed dam |  |  | 
# of fish that passed LGS | 367 | -
# of fallback fish | 36 | 9.8%
# of fallback events | 44 | 12.0%
# of fallback events through SP | 38* | 86.4%
# of fallback events through PH | 6** | 13.6%
upstream LGR | 32 | 88.9%
between LMN and LGS | 3 | 8.3%
downstream MCN | 1 | 2.8%
* 25 through ASW and 13 through regular spillway bays ** Three of the fish that had fallback through the PH were detected by the JBS PIT |  | 

## Slide 23: Fallback Time After Exiting Fish Ladder
Amount of time from 1st forebay detection to the last forebay detection prior to fallback.
Chart: Number of Fallback Events
| < 1 hr | 1 - 2 hr | 2 - 3 hr | 3 - 4 hr | 4 - 5 hr | > 5 hr
 | 24 | 5 | 1 | 1 | 0 | 13

## Slide 24: Total Flow and Spill Percentage at Time of Fallback Event
Chart: Total Flow (kcfs)
| 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170
 | 1 | 1 | 1 | 1 | 1 | 3 | 8 | 5 | 14 | 5 | 4
Chart: Spill Percentage
| 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004
 | 3 | 6 | 11 | 8 | 12 | 3 | 1

## Slide 25: Final Fate
 |  | Count | Percentage
Downstream ICH | Lower Columbia River | 11 | 2.75%
 | Walla Walla River | 1 | 0.25%
 | Upper John Day River | 1 | 0.25%
 | Upper Yakima River | 1 | 0.25%
Between ICH and LMN | Snake River | 2 | 0.50%
Between LMN and LGS | Snake River | 10 | 2.50%
 | Tucannon River | 6 | 1.50%
Between LGS and LGR | Snake River | 5 | 1.25%
Upstream of LGR |  | 357 | 89.25%

## Slide 26: Hourly Distribution of Adult Fish Entering Fish Ladder
Fish prefer to enter fish ladder during the day time
  95.26% of fish entered fish ladder after 4 am and before 7 pm.
2008 study also found that fish were most active during daylight hours and least active at night.

## Slide 27: Spill Level and Proportion of Fish in the Tailrace Entering Fish Ladder from 5/21 to 6/3
Results were calculated for day time spill period (4 am to 8 pm PDT).
From 5/21 – 5/24, when spill level was 35-40%, about 30-50% of fish in the tailrace entered fish ladder.
From 5/25 – 5/29, spill level was at 45% and above and less than 20% of fish in the tailrace entered the fish ladder.
From 5/30 - 6/3, special 30% spill treatment was applied.
  Over 40% - 65% of fish in the tailrace entered fish ladder during 30% spill treatment within these 4 days.
Chart: Spill Operation Period
# of fish detected in the tailrace | 75 | 48 | 41 | 28 | 39
# of fish entered FL | 32 | 16 | 14 | 5 | 12
spill | 0.3484 | 0.357 | 0.3765 | 0.43677 | 0.40034
Chart: Spill Operation Period
# of fish detected in the tailrace | 35 | 36 | 35 | 28 | 50 | 49 | 56 | 53 | 53
# of fish entered FL | 3 | 5 | 3 | 0 | 4 | 5 | 6 | 3 | 5
spill | 0.40042 | 0.45048 | 0.44963 | 0.48593 | 0.50004 | 0.43624 | 0.43192 | 0.4349 | 0.58077
Chart: Spill Operation Period
# of fish detected in the tailrace | 54 | 29 | 27 | 35 | 19 | 30 | 16 | 19 | 10
# of fish entered FL | 25 | 6 | 2 | 19 | 6 | 19 | 3 | 9 | 1
spill | 0.30192 | 0.40699 | 0.47093 | 0.29961 | 0.40524 | 0.30171 | 0.40628 | 0.29893 | 0.36463

## Slide 28: Spill Level and Proportion of Fish in the Tailrace That Entered North Fish Ladder and South Fish Ladder from 5/21 to 6/3
From 5/21 - 5/29, no clear trend of fish entering ladder through South and North Entrance
From 5/30 - 6/3, during the 30% spill treatment periods, more fish first entered through North Shore Entrance than South Shore Entrance.
Chart: Spill Operation Period
# of fish detected in the tailrace | 75 | 48 | 41 | 28 | 39 | 35 | 36 | 35 | 28 | 50 | 49 | 56 | 53 | 53
# of fish first entered North FL | 15 | 9 | 11 | 2 | 8 | 2 | 2 | 1 | 0 | 2 | 2 | 4 | 3 | 3
# of fish first entered South FL | 16 | 7 | 3 | 3 | 4 | 2 | 3 | 2 | 0 | 2 | 3 | 2 | 1 | 2
spill | 0.3484 | 0.357 | 0.3765 | 0.43677 | 0.40034 | 0.40042 | 0.45048 | 0.44963 | 0.48593 | 0.50004 | 0.43624 | 0.43192 | 0.4349 | 0.58077
Chart: Spill Operation Period
# of fish detected in the tailrace | 54 | 29 | 27 | 35 | 19 | 30 | 16 | 19 | 10
# of fish first entered North FL | 24 | 5 | 0 | 18 | 4 | 14 | 0 | 5 | 0
# of fish first entered South FL | 1 | 1 | 2 | 1 | 2 | 6 | 3 | 4 | 1
spill | 0.30192 | 0.40699 | 0.47093 | 0.29961 | 0.40524 | 0.30171 | 0.40628 | 0.29893 | 0.36463

## Slide 29: Fish Movement in Tailrace Relative to Spill Operations
A higher percentage of fish were first detected in the north shore than the south shore region within each of the spill treatments
  For higher spill percentages a larger percentage of fish were along the north shore
For fish that were first detected in the north shore region at lower spill percentage, about half stayed in the north shore region and the other half moved downstream or to the south shore
  As the spill percentage increased lower percentage of fish moved to other regions
At higher levels spill percentage, a lower percentage of fish entered the ladder
Chart: Fish Starting in North Tailrace During Spill Treatments
| 0.338391 | 0.38475900000000002 | 0.38232899999999997 | 0.63570800000000005 | 0.35787999999999998 | 0.38416699999999998 | 0.34839700000000001 | 0.35699799999999998 | 0.376496 | 0.43676799999999999 | 0.40034399999999998 | 0.40041500000000002 | 0.45048199999999999 | 0.449629 | 0.485933 | 0.50003600000000004 | 0.43623899999999999 | 0.43192000000000003 | 0.43490499999999999 | 0.580766 | 0.30192400000000003 | 0.40699400000000002 | 0.47092699999999998 | 0.29961399999999999 | 0.40523500000000001 | 0.301709 | 0.406281 | 0.29893199999999998 | 0.36463400000000001 | 0.21596499999999999
starting North and stay North (%) | 0.66667 | 0.42105 | 0.3125 | 0.56452 | 0.74576 | 0.69388 | 0.50877 | 0.59375 | 0.60606 | 0.86364 | 0.625 | 0.78125 | 0.72727 | 0.69697 | 0.96154 | 0.85106 | 0.84783 | 0.73077 | 0.98 | 0.88 | 0.40385 | 0.92308 | 1 | 0.46667 | 0.5625 | 0.6 | 0.58333 | 0.61538 | 0.4 | 1
starting North and moved between regions (%) | 0.33333 | 0.57895 | 0.6875 | 0.43548 | 0.25424 | 0.30612 | 0.49123 | 0.40625 | 0.39394 | 0.13636 | 0.375 | 0.21875 | 0.27273 | 0.30303 | 0.038462 | 0.14894 | 0.15217 | 0.26923 | 0.02 | 0.12 | 0.59615 | 0.076923 | 0 | 0.53333 | 0.4375 | 0.4 | 0.41667 | 0.38462 | 0.6 | 0
Chart: Fish Starting Location During Spill Treatments
| 0.338391 | 0.38475900000000002 | 0.38232899999999997 | 0.63570800000000005 | 0.35787999999999998 | 0.38416699999999998 | 0.34839700000000001 | 0.35699799999999998 | 0.376496 | 0.43676799999999999 | 0.40034399999999998 | 0.40041500000000002 | 0.45048199999999999 | 0.449629 | 0.485933 | 0.50003600000000004 | 0.43623899999999999 | 0.43192000000000003 | 0.43490499999999999 | 0.580766 | 0.30192400000000003 | 0.40699400000000002 | 0.47092699999999998 | 0.29961399999999999 | 0.40523500000000001 | 0.301709 | 0.406281 | 0.29893199999999998 | 0.36463400000000001 | 0.21596499999999999
starting_North (%) | 0.64286 | 0.73077 | 0.61538 | 0.91176 | 0.84286 | 0.80328 | 0.76 | 0.66667 | 0.80488 | 0.78571 | 0.82051 | 0.91429 | 0.91667 | 0.94286 | 0.92857 | 0.94 | 0.93878 | 0.92857 | 0.9434 | 0.9434 | 0.96296 | 0.89655 | 0.85185 | 0.85714 | 0.84211 | 0.66667 | 0.75 | 0.68421 | 0.5 | 0.5
starting_south (%) | 0.35714 | 0.23077 | 0.36538 | 0.088235 | 0.14286 | 0.19672 | 0.21333 | 0.33333 | 0.19512 | 0.17857 | 0.17949 | 0.057143 | 0.083333 | 0.057143 | 0.071429 | 0.06 | 0.061224 | 0.071429 | 0.037736 | 0.037736 | 0.018519 | 0.10345 | 0.074074 | 0.14286 | 0.15789 | 0.26667 | 0.1875 | 0.26316 | 0.3 | 0.41667
Chart: % of Fish Entered Fish Ladder
| 0.338391 | 0.38475900000000002 | 0.38232899999999997 | 0.63570800000000005 | 0.35787999999999998 | 0.38416699999999998 | 0.34839700000000001 | 0.35699799999999998 | 0.376496 | 0.43676799999999999 | 0.40034399999999998 | 0.40041500000000002 | 0.45048199999999999 | 0.449629 | 0.485933 | 0.50003600000000004 | 0.43623899999999999 | 0.43192000000000003 | 0.43490499999999999 | 0.580766 | 0.30192400000000003 | 0.40699400000000002 | 0.47092699999999998 | 0.29961399999999999 | 0.40523500000000001 | 0.301709 | 0.406281 | 0.29893199999999998 | 0.36463400000000001 | 0.21596499999999999
 | 0.35714 | 0.34615 | 0.44231 | 0.22059 | 0.15714 | 0.21311 | 0.42667 | 0.33333 | 0.34146 | 0.17857 | 0.30769 | 0.085714 | 0.13889 | 0.085714 | 0 | 0.08 | 0.10204 | 0.10714 | 0.056604 | 0.09434 | 0.46296 | 0.2069 | 0.074074 | 0.54286 | 0.31579 | 0.63333 | 0.1875 | 0.47368 | 0.1 | 0.41667

## Slide 30: Temperature Reduction System Pump On vs. Off - Travel Time from PIT Detection to Forebay

## Slide 31: Conclusions
The acoustic telemetry receivers deployed in the LGS tailrace resulted in high detection efficiency and provide good tracking results
More fish experienced fallback during 2018 (9.8%) compared to the 2008 (3.9%) and 2013 (7.5%) studies.
A majority (62%) of fish were first detected approaching the LGS tailrace along the north shore.
Slightly over half of the fish utilized the north shore fish ladder entrance, and just under half used the south powerhouse entrance. Only 3 (1%) fish used the north powerhouse entrance.
  In previous studies the north powerhouse entrance was always the least used, but the percentages were significantly higher (9% and 16%).
With higher proportions of spill this year, fish took more time to enter the LGS fish ladder.
In this study a larger percentage of fish reached the LGS tailrace than the previous studies, and of those fish a slightly higher percentage passed LGS.
30% spill treatments helped fish to enter the fish ladder and pass LGS. A higher percentage of tagged fish (40 – 65%) was observed entering the fish ladder at the 30% spill level than any other spill level.
When spill level was at 35 – 40%, about 30 – 50% of tagged fish were observed entering the fish ladder.
When spill level was at 45% and above, less then 20% of tagged fish were observed entering the fish ladder.
No difference was detected in travel time from being PIT detected to exiting into the forebay when the temperature reduction system pump was on or off.

## Slide 32: Acknowledgments
Funding support:
  US Army Corps of Engineers, Walla Walla District
U.S. Army Corps of Engineers:
  Derek Fryer, Chris Pinney, Scott St. John, Rick Weis, Ryan Laughery, Martin Ahmann
Pacific Northwest National Laboratory:
  Jun Lu, Aljon Salalila, Jarod Cable, Sam Harding, John Stephenson, Kyle Larson, Kate Deters, Bernardo Beirao, Jacqueline Wells, Ryan Ekre, Brian Bellgraph, Shon Zimmerman
U.S. Department of Energy for the funding of related technology development

## Slide 33
For additional information about JSATS:
http://jsats.pnnl.gov