## Slide 1: North Santiam Temperature Task Group W-FPOM
October 26, 2016

## Slide 2: North Santiam Temperature Targets Current vs. Proposed
Chart: Water Temperature (Co)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Current (max) | 40.1 | 42.1 | 42.1 | 45.1 | 49.1 | 56.1 | 61.2 | 60.3 | 56.1 | 50 | 50 | 41
Current (min) | 40.1 | 41 | 41 | 43.2 | 46 | 51.1 | 54.1 | 54.1 | 52.3 | 50 | 50 | 41
Proposed (max) | 42 | 42 | 44 | 46 | 50 | 54 | 54 | 54 | 54 | 52 | 46 | 46
Proposed (min) | 38 | 38 | 42 | 42 | 46 | 48 | 48 | 48 | 48 | 46 | 42 | 41
Notes: ESA, BiOp, RPA, late, not much pressure, more interest lately

## Slide 3: Normal Year

## Slide 4: Cool Wet Year

## Slide 5: Hot Dry Year

## Slide 6: Spring Chinook Evaluation
Notes: Proposed better for spawning, worse for incubation

## Slide 7: Winter Steelhead Evaluation
 |  |  |  |  | Existing |  |  |  | Proposed | 
Alternative Evaluation | Date Range | Impact Type | criteria (deg. C) | criteria (deg. F) | cool wet | hot Dry | normal | cool wet | hot Dry | normal
 |  |  |  |  | percent of days not achieving criteria |  |  |  |  | 
Incubation | Mar-01 to Jun-30 | Sub-opitimal | > 10.0 | > 50.0 | 17 | 26 | 24 | 17 | 30 | 23
Notes: Emergence dates equal

## Slide 8: July and August Max Target (58oF) Normal Year

## Slide 9: July and August Max Target (58oF) Hot Dry Year

## Slide 10: 2016 Water Temperatures

## Slide 11: Summary and Discussion
Proposed targets appear a little better for spawning, a little worse for incubation (ChS), differences are minimal compared to current
Proposed minimum target a concern Jun-Sep (potential migration delay, ChS)
Cooler temps better for fish health at Minto FF and in the river
Impacts between Current vs Proposed were essentially Equal for StW (very similar emergence timing)
Next Steps/Thoughts:
  Vary approach depending on water year
  Maybe set max target Jul-Aug 58oF during warmer years
  Use 54oF as max target Jul-Aug (normal & cooler years)
  Maybe set min target Jul-Aug between 50-52oF (minimize potential delay)
  Engage DET Temperature PDT
  Bennett and Willamette counts
  Meet again ???, or brief at W-FPOM
Notes: Newer ODFW targets (cooler for July and Aug), essentially equal to current regime