## Slide 1: Cougar Downstream Passage Alternatives Screening
26 June 2017

## Slide 2: Meeting purpose
    Discuss Alternatives Decision Matrix

## Slide 3: Alternative Decision matrix - Elements and Options
Configuration | ID | Description
Alternative 1 | A1 | Single Entrance Inline FSS
Alternative 2 | A2 | Dual Entrance Angled FSS
Alternative 3 | A3 | Dual Entrance Inline FSS
Mooring Options |  | 
Alternative 1 | M1 | Stair Tower with Two Dolphins
Alternative 2 | M2 | Three Dolphins
Fish Transport Options |  | 
Alternative 1 | F1 | Mono Rail System
Alternative 2 | F2 | Amphibious Vehicle (AV)
Alternative 3 | F3 | WTCT Side Rail
Crew Access Options |  | 
Alternative 1 | C1 | Walkway to Stair Tower, then down stair tower
Alternative 2 | C2 | Amphibious Vehicle plus alt. personnel access
Alternative 3 | C3 | Stair Tower on WTCT, which requires employees to walk down the outside of the WTCT
Screening Criteria (16 total sub-criteria)
  Biological (4 sub-criteria)
  Environmental (3 sub-criteria)
  Dam Safety (1 sub-criteria)
  O&M (6 sub-criteria)
  Constructability & Design (2 sub-criteria)

## Slide 4: Review alternatives
    Refer to alternatives PDF

## Slide 5: Option Scoring Exercise: 0-5 Scale in 0.5 increments 0= N/A 1= Option does not meet Criteria 5= Option meets criteria to full extent
 |  |  | BIOLOGICAL CRITERIA |  |  |  |  |  |  | 
Element | ID | Measures | Location: Is the entrance(s) located in areas were the fish congregate? | Score | Attraction Flow: Does this option provide for a signature out front of the FSS at the full range of pool elevations? | Score | Capture Potential: Does this option promote fish collection potential based on professional judgement or studies? | Score | Interferences/Distractions/Competing Flows: Does this option create a conflict for fish or flow? | Score
Configuration | A1 | Single Entrance Inline FSS | Unsure if the fish would find the outlet if the location is moved. Are the fish following the flow or the shoreline? |  | Depends if all flow going through the FSS. Expect that at the lower elevations we will be exceeding 1000cfs on average. Could Rush Creek be considered a competing flow. More information needed bio and hydro input. |  |  |  | Could be a perceived predator hangout. This may be better addressed under attraction flow. | 
 | A2 | Dual Entrance Angled FSS |  |  |  |  |  |  |  | 
 | A3 | Dual Entrance Inline FSS |  |  |  |  |  |  |  | 
Decision Making Process
Vote on Score, majority rules (16 PDT members voting)
If vote is split close to middle, take average
If someone strongly disagrees they will have 2 minutes to defend their score
Revote
If descent it still strong, parking lot vote on that criteria and come back
Review Parking lot items – majority rules

## Slide 6: Alternatives Formulation and Screening
54 Initial Alternative Combinations
Fish Transport and Crew Access Options are dependent (F1 must go with C1); therefore, alternatives with wrongly paired combinations were screened out
15 Final Alternative Combinations remained (top 10 shown)
Preferred alternatives: Dual entrance/angled FSS (entrance location to be refined), three dolphins, and amphibious vehicle for fish transport and crew access
Alternative | Total Score (sum of Total sub-criteria scores for options in Alts) (205 max) | Biology Criteria (sum of Biology sub-criteria scores for options in Alts) (30 max) | Biology Criteria (sum of Biology sub-criteria for configuration only) (20 max) | RANK (highest to lowest score)
A2M2FC2 | 133.5 | 22.5 | 15.5 | 1
A3M2FC2 | 133 | 19.5 | 12.5 | 2
A1M2FC2 | 130 | 15.5 | 8.5 | 3
A2M2FC3 | 105 | 19.5 | 15.5 | 4
A3M2FC3 | 104.5 | 16.5 | 12.5 | 5
A2M1FC3 | 102.5 | 19.5 | 15.5 | 6
A3M1FC3 | 102 | 16.5 | 12.5 | 7
A1M2FC3 | 101.5 | 12.5 | 8.5 | 8
A1M1FC3 | 99 | 12.5 | 8.5 | 9
A2M2FC1 | 97.5 | 19.5 | 15.5 | 10